TAQOZ Reloaded v2.8 - Writing Inline Assembly Code
TAQOZ Reloaded is a powerful language, so why inline assembly code?

- When your TAQOZ Reloaded application still runs too slowly e.g. when streaming audio or video. After measuring execution times of words in the critical path with LAP and .LAP, converting some of those words to assembly language may get you within spec. Aim to do the minimum necessary.
- TAQOZ Reloaded with it's inline assembler makes a highly interactive sandbox to experiment with various functions, reducing development time.
- There is often no need to write a test harness around the function under test - just manual entry from the TAQOZ command line is enough to check the function is working. Your edit-compile-test cycle is much quicker than other languages - as each word comes to life. More fun means you may be more productive.

There is a downside - each assembly language instruction consumes 32 bits of memory whereas TAQOZ high level words only need 16 bits. The assembler takes up precious space in memory.

The TAQOZ Interactive Assembler (TIA) in TAQOZ Reloaded is intended for creating relatively short pieces of assembly code, in line with good forth practice. No awful 'War and Peace' sized functions, thank you very much.

The following notes were enough baby steps to get me writing inline code for a dsp project.
# Obtaining the Assembler
Check that the assembler is already present in your tool set. If the TAQOZ Reloaded start up message includes something like...

4890 *P2ASM* TAQOZ INTERACTIVE ASSEMBLER for the PARALLAX P2 - 210124-1200

...then the assembler is already there. Otherwise, from the Tachyon Forth dropbox, find P2ASM.FTH in folder Tachyon/P2/TAQOZ/Forth. Upload this file to TAQOZ and check it compiles with no errors. You can optionally keep the assembler resident in the tool set by typing BU <enter> to back up the complete system.
# P2 Reference Documents
The P2 instruction set, Assembly Language Manual and the Propeller 2 Documentation are essential aids to inline assembly programming. A paper Tachyon Forth Model by Peter Jakacki is also useful.

# Instruction Syntax
P2 instructions in general are written as:-
{_RET_} or / { conditional }	ROR	Destination,	{#}Source	{wc/wz/wcz}
optional return to TAQOZ or a conditional	Instruction name		Optional # denotes constant value	Optional flags affected as a result of the instruction

Any instruction may be made conditional with:-

Conditional name including aliases	Flags
if_nz_and_nc / if_a / if_00 / if_nc_and nz	nc & nz
if_z_and_nc / if_01 / if_nc_and_z	nc & z
if_ae / if_0x / if_nc	nc
if_nz_and_c / if_10 / if_c_and_nz	c & nz
if_ne / if_x0 / if_nz	nz
if_z_ne_c / if_diff / if_c_ne_z	c <> z
if_nz_or_nc / if_not_11 / if_nc_or nz	nc | nz
if_11 / if_z_and_c / if_c_and_z	c & z
if_same / if_z_eq_c / if_c_eq_z	c = z
if_e / if_x1 / if_z	z
if_z_or_nc / if_not_10 / if_nc_or_z	nc | z
if_b / if_1x / if_c	c
if_not_01 / if_nz_or_c / if_c_or _nz	c | nz
if_not_00 / if_be / if_z_or_c / if_c_or_z	c | z

N.B. Totally blank lines are not permitted within an assembly definition - Christof Eb reports they cause 'stack mismatch' error messages from the Assembler.
# Defining an inline assembly word
A simple inline assembly word is bracketed with code and end like this:-
code MYCODE 'keyword 'code' followed by the name of the new word / ( assembly words ) / ret 'return to the TAQOZ interpreter / end 'keyword 'end' signals the end of the assembly word

# Back and Forth within the Definition
The words ASM: and FORTH: make possible the mixing of forth and assembly code in the same definition. e.g.
pub MYWORD ( ch -- ) --- N.B. This currently does not work – word FORTH: is buggy / ... forth words ... / ASM: / ... assembly language / FORTH: / .. forth words ... / ;

or

pub MYWORD ( ch -- ) / ... forth words ... / ASM: / ... assembly language / jmp #\@<forth word name> or ret / end

Here’s a working example of this, created by Christof Eb on the Parallax forum, which should get you going with your own ‘mixed’ words:-

FORTH ASSEMBLER / pri PCNEXT _pc @ 12 + ; / ' CALL 8 + W@ 1- := doNEXT --- points to the start addr of the forth interpreter / pub FORTH: --- bug fix for FORTH: word / end [C] ] ; / FORTH / : testD ( – ) --- test word for mixed assembler and forth / 1 --- initialise a counter with the value 1 on the data stack / begin / ASM: / add a,#1 --- counter now 1 + 1 = 2 / mov PTRA,##PCNEXT / jmp doNEXT / FORTH: / crlf dup . / ASM: / add a,#1 --- add 1 to the counter / mov PTRA,##PCNEXT / jmp doNEXT / FORTH: / crlf dup . --- copy and display the counter / 1000 ms --- do nothing for 1 s / dup 10 > until --- and loop to begin until counter = 11 / drop --- clean up the data stack / ;

# TAQOZ register usage

The following registers are available for use within inline assembly language:-

xx
yy
zz	also known as	r0 or r1
r2
r3
r4
acc	also known as	ac

ptra	useful for indexing arrays and strings
ptrb	useful for indexing arrays and strings - used by TAQOZ so value needs preserving

During the reading or writing of data to hub memory, ptra and ptrb can incremented and decremented by the correct number of bytes using the following keywords:-

ptra	points to the address, no pointer increment or decrement
ptra++ after the instruction has executed, ptra is incremented by byte, word or long as appropriate
++ptra	before the instruction executes, ptra is incremented by byte, word or long as appropriate
ptra--	after the instruction has executed, ptra is decremented by byte, word or long as appropriate
--ptra	before the instruction executes, ptra is decremented by byte, word or long as appropriate

The same grammar applies to ptrb e.g ptrb++ or --ptrb
## Kernel registers
Defined registers in the forth kernel are:-

_depth, _pin, sck, mosi, miso, ss, reg4, reg5, reg6

# Labels
To enable jumps in an assembly based word, TIA provides 8 fixed name labels l0 to l7 (lowercase L) which is plenty, because they can all be reused once each definition is complete. This is the syntax for labels:-
code MYWORD / ... assembly language .. / .l2 ... assembly language ... ' this line has a label l2 / ... assembly language ... / djnz r1,#l2 ' this line includes a jump to l2 / ret / end

N.B. Backward jumps can be made using any type of jump instruction. Forward jumps are only supported for the DJNZ instruction. Thanks for that tip, Christof Eb. Christof also mentions that the SKIP instruction can be useful for forward jumps e.g.
cmp d,#2 wz / if_z skip #%11111111 ' skips next 8 instructions

# Looping Macros
As an aid to creating loops in a more high level fashion, these macros are aimed at easing a new assembly language user into simple looping without fuss. They're not as versatile as the various branching assembly language instructions and they don't translate to other languages that support inline coding.
## The FOR: NEXT: macros
Example code:-
code ffibo ( n1 -- n2 ) ' n2=n1'th fibonacci number / mov xx,#0 / mov yy,#1 / FOR: / add yy,xx / djnz a,#l2 / _ret_ mov a,yy / .l2 add xx,yy / NEXT: a / _ret_ mov a,xx / end

So the 'NEXT: a' statement decrements a ( the top of data stack ) and jumps back to the 'FOR:' statement if a is non-zero.

## The BEGIN: AGAIN: UNTIL: macros

BEGIN: ... AGAIN: is an endless loop and is used like BEGIN ... AGAIN in high level Taqoz.
BEGIN: .... UNTIL: <condition> is a loop that ends, where <condition> is one of WC , WZ or WCZ

# The Data Stack
top of stack is named as	a
tos + 1 is named as	b
tos + 2 is named as	c
tos + 3 is named as	d
## Words that don't alter the stack depth
The less the stack is disturbed, the better from a speed point of view. If it can be arranged that the stack depth doesn't change, then the inline word will run the fastest. So, a word to double the value on the top of stack is:-

code MYDOUBLE ( n1 -- n2 ) 'n2 = n1 * 2 / _ret_ shl a,#1 'shift tos one place left and return to TAQOZ / end

Notice that the ret to the TAQOZ interpreter is combined with the last instruction.

Here's a more complicated example that multiplies two 32 bit unsigned values together to produce a 64 bit result. Notice there are two input parameters and one output parameter. However the inputs take up the same space as the output, so the stack depth doesn't need to change:-

code MUL ( b a -- a*b as a double ) / getword xx,a,#1 / getword yy,b,#1 / mov zz,xx / mul zz,yy / mul xx,b / mul yy,a / add xx,yy wc / getword yy,xx,#1 / bitc yy, #16 / shl xx,#16 / mul a,b / add xx,a wc / addx yy,zz / mov b,xx / _ret_ mov a,yy / end

## Dropping values from the stack
This example makes a jump to @DROP to drop the top value from the stack and return to the TAQOZ interpreter. This example also shows two TAQOZ constants being used in the inline word:-

56 := SCL / 57 := SDA / code MYTX16 '( word -- ) / rev a / shr a,#16 / wypin a,#SDA / wypin #32,#SCL / jmp #@DROP 'an equivalent macro is DROP; / end

To drop the top two values, use relative address jmp #@2DROP
To drop the top three values use jmp #@3DROP
The @ is interpreted as "find the address of <forth definition>", so very useful.

To jump to an absolute address write this as "#\@DROP" :-
code WSTX / ... assembler language ... / jmp #\@2DROP / end

These endings are used often, so there are three macros DROP; 2DROP; and 3DROP; that can be substituted for the 'jmp #@DROP end' lines.
## Pushing new values to the stack
When your word needs more space on the stack for results e.g. Here's a function that needs no inputs, but just pushes the value 1 to top of stack:-

code ONEOFAKIND / >PUSHX ' make room for a new tos entry / _ret_ mov a,#1 ' and set that entry = 1 / end

## Other convenience words

Other convenience words used like >PUSHX are:-

>ROT	( a b c -- b c a )	move the third entry to top of stack
>SWAP	( n1 n2 -- n2 n1 )	swap the top two stack entries
>I	( -- n1)	returns the current loop index n1
>SPIRD	( n1 -- n2 )	Read 8-bits left into n1 so that n2 = n1<<8+new. Four successive SPIRDs will receive 32-bits
>SPIWB	( byte -- )	Shift 8 bits from data[0..7] out and leave data on stack (restored with other bytes zeroed)
>SPICE	( -- )

# Reading and Writing to hub Memory
There are three memory regions: cog RAM, lookup RAM, and hub RAM. Each cog has its own cog RAM and lookup RAM, while the hub RAM is shared by all cogs. (RAM - random access memory)

Memory / Region	Memory Width	Memory Depth	Instruction D/S Address Ranges	Program Counter Address Ranges
COG	32 bits	512	$000..$1FF	$00000..$001FF
LOOKUP(LUT)	32 bits	512	$000..$1FF	$00200..$003FF
HUB	8 bits	1,048,576 (*)	$00000..$FFFFF	$00400..$FFFFF

So this is writing and reading to a long variable in hub memory (read and write word or byte would be very similar):-

long MYVARI / code MYWRITE ( n1 -- ) ' writes n1 to variable MYVARI / wrlong a,#MYVARI / jmp #\@DROP ' you can just use DROP; here / end / code MYREAD ( -- n1 ) / >PUSHX 'make room for the result / _ret_ rdlong a,#MYVARI ' set tos=MYVARI / end

## Using indirect addressing to make a more useful function
Reading and writing to a specifically named variable is OK for accessing global variables, but more usual is to read and write to an address supplied as an input on the stack. This makes for a more useful word to access any variable:-

code MYINC ( adr --- ) ' increment long at adr / mov PTRA,a ' PTRA = adr / rdlong a,ptra ' read long at adr / add a,#1 ' increment the long / wrlong a,ptra ' write it back to the adr / DROP; / end

## Using indirect addressing to work on arrays
This is where assembly language really starts to pay off in speed: e.g. A dsp application requires numerous looped functions to work on arrays of signal data. These looped functions are written in assembly code. The result is that most of the processors' time is spent in the loops doing the dsp maths and very little time is spent in the TAQOZ interpreter between the dsp words. The application is written in TAQOZ, but runs nearly as fast and efficiently as an all-Assembly application. BUT, it's been written and tested one function at a time - so much less of a monster to commission.
Here's an inline assembly word and identical forth word, working on a byte array:-

100 bytes KAKA / ' increment all elements of byte array at adr / code MYINC '( arraysize array -- ) / mov PTRA,a ' PTRA = adr / .l0 ' start our array processing loop / rdbyte a,ptra ' read byte at adr / add a,#1 ' increment the byte / wrbyte a,ptra++ ' write it back to the adr and increment PTRA / djnz b,#l0 ' and do above for all array elements / 2DROP; / end / ' increment all elements of byte array at adr / pub MYINCFORTH ( arraysize array -- ) / SWAP / FOR / DUP I + --- calculate the address / C++ --- increment array elements / NEXT / DROP --- and clean up / ;

Compare the speed of the forth versus inline assembly:-

TAQOZ# 100 KAKA LAP MYINC LAP .LAP --- 5,096 cycles= 25,480ns @200MHz ok / TAQOZ# 100 KAKA LAP MYINCFORTH LAP .LAP --- 38,136 cycles= 190,680ns @200MHz ok / TAQOZ# 38136 5096 / . --- 7 ok

So, around a 7x improvement in speed achieved using only 'rooky' code knowledge.
# Running code from COG RAM

Christof Eb from the Parallax forum provided this very useful coding tip: If you really want a TAQOZ word to run as fast as possible, then it can be run from COG Ram. This executes faster than Hub Ram. Here we define a 'test' word to try it out:-

code test ( value n -- value+3*n 0 ) / add b,#3 / sub a,#1 wz / if_nz jmp #\@COGMOD ' loop from start / ret / end

Now we copy this 'test' word from Hub Ram to COG Ram with the command:-
AT test 2+ 4 LOADMOD \ loads the asm instructions of 'test' into COG Ram

Now we can execute the code from COG Ram with:-
10 5 COGMOD . . \ executes the loaded code

Nice one!

Currently, LOADMOD / COGMOD uses COG Ram starting at $1CB. When tested, a code word containing up to 40 instructions can be transferred to COG Ram. Any more than that and TAQOZ stops working.
# Other Links
- MEDIA.FTH located in folder TAQOZ/Forth in the Tachyon Forth Files makes quite a lot of use of inline code and is worth looking at for further examples.
- There is a TAQOZ Interactive Assembler thread in the Parallax forum. Be warned, early examples of code won't run without editing, as the TIA syntax evolved.
- My CREATE DOES> inline code included in this SI5351 driver
- My Locks and WAITATN inline code
# Conclusion
The above has been a quick introduction to creating inline assembly words using TIA in TAQOZ Reloaded. The paper was written as reminder notes whilst the author was getting familiar with the subject. This will be revised from time to time, to jot down handy techniques as more is learned.

Bob Edwards, retired EMC engineer in SW U.K., ham radio call G4BBY April 2022
# Appendix 1 CREATE ... DOES>
These two words allow the user to expand the TAQOZ compiler – often useful around assembly language:-

 --- CREATE ... DOES> FOR TAQOZ V2.8 VER 2
{
CREATE / DOES> is the pearl of the Forth programming language, enabling the definition of new 'defining' words,
thus extending the compiler to suit the application - a very powerful feature. Here we test the new words out with a new data type,
WARRAY, a single dimension word array
}

--- create new dev with dummy cfa (save ptr to it)
pub CREATE	( -- )
[C] GRAB
[C] CREATE: --- Using the next word in the input stream as the name, create a VARIABLE type dictionary entry
    [C] GRAB	--- make sure CREATE: has run before anything more
   HERE 2- 0 REG W!	--- save the address of the code after DOES> in the REG scratchpad area
;

--- set new cfa to point back to DOES: code (skipped by DOES: itself)
pub DOES>	( -- )
    R>	--- the first word location in the new word being defined
    0 REG W@	--- retrieve the address stored on scratchpad
    W!	--- set the first word to execute as the address of the code after DOES>
;

--- example definition of a new 'array of words' data type - no bounds checking
pre WARRAY
    CREATE ( cnt -- )
        FOR
        0 [C] ||
        NEXT	--- Create cnt bytes set to 0
    DOES> ( index -- addr )
        2* R> +	--- the address of the first byte + index = the entry reqd
;

--- Create a new array MYARRAY1 which can hold 10 word sized values
10 WARRAY MYARRAY1

--- now lets check the array addresses are formed correctly
0 MYARRAY1 .
1 MYARRAY1 .
2 MYARRAY1 .
3 MYARRAY1 .

--- now check write and read data works
: TEST1 ---
10 FOR I I MYARRAY1 W! NEXT ---
10 FOR I MYARRAY1 W@ . SPACE NEXT ---
;

# Appendix 2 - Cog Synchronisation

--- Extension to Synchronising Execution between COGS ver1 for Taqoz Reloaded v2.8 - Bob Edwards May 2021

--- Pause execution waiting for an ATN flag from another cog
--- The cog waits for the ATN flag for up to 'clocks' ticks.
--- If ATN occurs before timeout, 'flag' = 1, else if timedout, 'flag' = 0
code WAITATN	( clocks -- flag )
getct xx	' read the bottom half of the 64 bit system counter
add a,xx
setq a	' timeout set for when the system counter = a
waitatn wc	' wait for atn flag
_ret_	wrnc a	' a = carry flag
end

--- Just loop until an ATN flag is received, using POLLATN
pub SLAVE1	( -- )
BEGIN
POLLATN
IF
." Slave1 received ATN, thanks!" CRLF
ELSE
250 ms
." Slave1, no ATN seen this time" CRLF
THEN
AGAIN
;
pub SLAVE2	( timeout -- )
BEGIN
200000000 WAITATN
IF
." Slave2 received ATN, thanks!" CRLF
ELSE
." Slave2 timed out!" CRLF
THEN
AGAIN
;

--- Output a message to show the MASTER looping. Set cog 5 AND 6
 ATN flag on each pass
: MASTER	( -- )
BEGIN
200 ms
." Hello from the Master, wake up cog 5 & 6
" CRLF
%1100000 COGATN	--- Send ATN to cog 5 and 6
KEY
UNTIL
;

--- set master and both slaves going
pub DEMO	( -- )
%ERSCN %HOME
%BOLD ." Press any key to stop" %PLAIN CRLF
' SLAVE2 5 RUN
' SLAVE1 6 RUN
MASTER
5 s
5 COGSTOP
6 COGSTOP
%BOLD ." The Slave loops were synchronised to ATN flags from the Master, until it was stopped" CRLF
." after which, they free-ran because they were no longer receiving those flags" %PLAIN CRLF
;

# Appendix 3 - Patch for SETEDG and POLLEDG
--- SETEDG and POLLEDG use setse1, but this is already in use by the terminal input, so these two words don't work properly
--- this patch redefines the two words to use setse2 and pollse2 - Bob Edwards May 2021

--- useful edge definitions
1 := rising
2 := falling
3 := changing

--- sets event for 'edge' = rising, falling, changing, on SmartPin 'pin'
--- original SETEDG used se1 which is already used in the serial port
code SETEDG	( edge pin -- )
shl b,#6
add a,b
setse2 a
2DROP;
end
--- e.g. use as 'rising 6 SETEDG' etc

--- redefinition of POLLEDG - polls for the SETEDG event
--- flag = TRUE if event occurred, else flag = FALSE
code POLLEDG	( -- flag )
>PUSHX
pollse2 wc
wrnc a
_ret_	sub a,#1
end
# Appendix 4 - Locks
--- LOCKS v1 for Taqoz Reloaded v2.8 - Bob Edwards May 2021

--- If two or more cogs are writing to the same data in hub memory, that data would be in jeopardy from race conditions as each cog performs
--- its read-modify-write cycle. The outcome of two cogs writing to the same address at very nearly the same time is unknown - which of the
--- two values ends up at the address?

--- To fix that, the P2 has a pool of 16 semaphore bits called locks....

--- Allocate a lock, returning the lock number n. If n = 0-15, lock was allocated, if n=-1 then all locks were already allocated
code LOCKNEW ( -- n )
>PUSHX	'make space on the stack
locknew a wc	't.o.s. new lock allocation number
if_nc	ret	'successful allocation
_ret_	mov a,#-1	'else signal all locks taken
end

--- Return lock number n (0-15) to the pool
code LOCKRET ( n -- )
lockret a
DROP;
ret
end

--- test LOCKNEW & LOCKRET

CRLF 17 FOR LOCKNEW . CRLF NEXT	--- try allocating one too many locks
13 LOCKRET CRLF ." Did we release lock 13? - " LOCKNEW	--- check we can release a lock
CRLF 16 FOR I LOCKRET NEXT	--- return all locks

--- Attempt to 'take' Lock n, flag = 0 if successful, else flag = 1
code LOCKTRY	( n -- flag )
locktry a wc
_ret_	wrnc a	' a = carry flag
end

--- Release Lock n (0-15) - only the cog that took the lock is permitted to do this
code LOCKREL	( n -- )
lockrel a
DROP;
end

--- Read lock n status, lock_status 1 = unlocked, 0 = locked - N.B. if lock is not owned, results invalid
code LOCK?	( n -- lock_owner lock_status )
>PUSHX	' make room for status
lockrel b wc	' t.o.s.+1 = cog no. whose lock it is
_ret_	wrnc a	' t.o.s. = lock status
end

long LOCKNUM1
long LOCKNUM2

pub SLAVE1 ( -- )
BEGIN
BEGIN
LOCKNUM1 @ LOCKTRY
30 ms
0= UNTIL
." Slave acquired lock" CRLF
500 ms
LOCKNUM1 @ LOCKREL
." Slave released lock" CRLF
500 ms
AGAIN ;
pub SLAVE2	( -- )
BEGIN
BEGIN
LOCKNUM2 @ LOCKTRY
30 ms
0= UNTIL
500 ms
LOCKNUM2 @ LOCKREL
500 ms
AGAIN
;

pub SLAVE3 ( -- )
BEGIN
BEGIN
LOCKNUM1 @ LOCKTRY
30 ms
0= UNTIL
750 ms
LOCKNUM1 @ LOCKREL
750 ms
AGAIN
;

pub MASTER ( -- )
BEGIN
BEGIN
LOCKNUM1 @ LOCKTRY
30 ms
0= UNTIL
." Master acquired lock" CRLF
1000 ms
LOCKNUM1 @ LOCKREL
." Master released lock" CRLF
1000 ms
KEY UNTIL ;pub .LOCKS	( -- )
OFF %CURSOR
BEGIN
%ERSCN %HOME
%BOLD ." Press any key to stop scanning..." %PLAIN CRLF
16 FOR
." Lock number " I . SPACE
I LOCK? SWAP
." owned by cog #" . SPACE
." status is " . CRLF
NEXT
20 ms
KEY UNTIL
ON %CURSOR
;

--- Demo the use of LOCK? to monitor Lock status in the P2
pub DEMO1	( -- )
LOCKNEW
LOCKNUM1 !
LOCKNEW
LOCKNUM2 !
' SLAVE2 5 RUN
' SLAVE3 6 RUN
.LOCKS
5 COGSTOP
6 COGSTOP
%BOLD ." So Cog 5 and 6 were monitored, by means of the LOCK? word, taking and releasing two locks" %PLAIN CRLF
LOCKNUM1 @ LOCKRET
LOCKNUM2 @ LOCKRET
;

--- Demo two cogs using a lock - each waits to take the lock in turn, then releases it
pub DEMO2	( -- )
LOCKNEW
LOCKNUM1 !
%ERSCN %HOME
%BOLD ." Press any key to stop the Master - 5s later the Slave will stop too" %PLAIN CRLF CRLF
' SLAVE1 5 RUN %ERLINE
MASTER
%BOLD ." Master stopped " CRLF %PLAIN
5 s
5 COGSTOP
%BOLD ." Slave also stopped" CRLF
." Any code sequence protected by the lock could only have been run BY ONE COG AT A TIME" CRLF
." so any read-modify-writes would run undamaged by the other cog. Enables race-free data" CRLF
." or orderly sharing of a subsystem - e.g. the console port" CRLF
%PLAIN
LOCKNUM1 @ LOCKRET
;

# Appendix 5 - Output to a Pin - high level code versus assembly language
With the cpu clock set to 200MHz this is high level code to toggle pin 10 high and low :-

: TEST BEGIN 10 HIGH 10 LOW AGAIN ;

Pin 10 goes high for 485nS and low for 675nS.

The equivalent in assembly language might be:-

code CTEST
mov a,#10	' pin 10
.l1	drvh a
drvl a
drvh a
drvl a	' output two +ve pulses
jmp #l1
ret
end

Pin 10 goes high for ~10nS and low for the same time. The jump however takes around 120nS, so quite slow by comparison with the 'linear' instructions.