# PUNYFORTH v0.5 GLOSSARY ------ for the ESP8266 Wifi module
The purpose of this glossary is to provide a sorted list of words, their stack effects, and a short description for Punyforth for the ESP8266 hardware. It is recommended to go to the relevant source code to glean more information if necessary.

Stack notation shows input parameters with the rightmost being the top of the stack, input parameters on the left, output on the right, separated by --
Where a word has a compile time and a run time behaviour, the two stack effects are shown as <compile effect> ; <runtime effect>

e.g. ( a b -- c )	A word removes the top two stack items as input parameters, b is top of stack (tos). The word places c on the stack as the result
e.g. ( n -- ; -- adr ) During compilation this word removes n from the stack. During execution the word leaves an address on the stack
e.g ( <text> n -- ) This word expects another word it will consume from the input stream and n that it will pop off the stack as inputs

The Code Type column is coded as follows - C - Assembly language word or H - High level word
Located in File indicates in which source file the definition can be found

Data is referred to as bytes (8 bits), words (16 bits), longs (32 bits) and doubles (64 bits). The Punyforth stacks are 32 bit wide, so types other than longs are padded or split when placed on the stack
# CORE WORDS
This section lists all the core words in Punyforth. These are words that are always available in the dictionary to write programs with.

NAME	STACK CODE LOCATED	DESCRIPTION
        TYPE IN FILE
## DATA STACK
_s0	( -- adr )	C	words.s	Address of stack pointer
-rot	( n1 n2 n3 -- n3 n1 n2 )	C	ext.s	tos moved to 3rd entry
?dup	( n -- n n ) if n<>0 else ( n -- n )	H	core.forth	if n <> 0, then duplicate n
2drop	( n1 n2 -- )	C	ext.s	drop top 2 entries from stack
2dup	( n1 n2 -- n1 n2 n1 n2 )	C	ext.s	duplicate top 2 entries from stack
2over	( n1 n2 n3 n4 -- n1 n2 n3 n4 n1 n2 )	C	primitives.s	copy 3rd and 4th entry to tos
2swap	( n1 n2 n3 n4 -- n3 n4 n1 n2 )	C	primitives.s	swap top two pairs
3drop	( n1 n2 n3 -- )	H	core.forth	Remove the top 3 items on the stack
3dup	( n1 n2 n3 -- n1 n2 n3 n1 n2 n3 )	H	core.forth	Duplicate the top 3 items on the stack
4drop	( n1 n2 n3 n4 -- )	C	ext.s	drop top 4 entries from stack
depth	( -- n )	H	core.forth	returns the present depth of the statck
drop	(n -- )	C	primitives.s	remove tos
dup	(n -- n n )	C	primitives.s	copy tos
nip	( n1 n2 -- n2 )	C	words.s	Drop 2nd entry from stack
over	( n1 n2 -- n1 n2 n1 )	C	ext.s	copy 2nd entry to tos
rot	( n1 n2 n3 -- n2 n3 n1 )	C	primitives.s	rotate 3rd entry to tos
s0	( -- adr )	H	core.forth	returns the address of the bottom of the stack
sp!	( adr -- )	C	primitives.s	set stack pointer to adr
sp@	( -- adr )	C	primitives.s	read stack ptr adr
swap	(n1 n2 -- n2 n1 )	C	primitives.s	swap top two entries
tuck	( n1 n2 -- n2 n1 n2 )	C	words.s	Copy tos under 2nd entry

## RETURN STACK
_r0	( -- adr )	C	words.s	returns address of return stack pointer
>r	( n -- )	C	primitives.s	pop tos and place on return stack
r@	( -- n )	C	ext.s	copy top of rstack to tos
r>	( -- n )	C	primitives.s	pop n from return stack and place tos
r0	( -- adr )	H	core.forth	returns the address of the bottom of the return stack
rdepth	( -- n )	H	core.forth	returns the present depth of the stack
rp!	( adr -- )	C	primitives.s	set return stack pointer to adr
rp@	( -- adr )	C	primitives.s	read return stack ptr adr

## LOGICAL
and	( n1 n2 -- n3 )	C	primitives.s	n3 = n1 and n2
invert	( n1 -- n2 )	C	primitives.s	n2 = not n1 - all bits inverted
nop	( -- )	H	core.forth	Do nothing
or	( n1 n2 -- n3 )	C	primitives.s	n3 = n1 or n2
rshift	( n shift -- )	C	primitives.s	Shift n 'shift' places right
xor	( n1 n2 -- n3 )	C	primitives.s	n3 = n1 xor n2

## COMPARISON
<	( n1 n2 -- flg )	C	primitives.s	flg = true if n1 < n2
<=	( n1 n2 -- flg )	C	primitives.s	flg = true if n2 less than or equal n1
<>	( n1 n2 -- flg )	C	primitives.s	flg = true if n2 not equal n1
=	( n1 n2 -- flg )	C	primitives.s	flg = true if n2 equal n1
>	( n1 n2 -- flg )	C	primitives.s	flg = true if n1 > n2
>=	( n1 n2 -- flg )	C	primitives.s	flg = true if n2 greater than or equal n1
0<	( n1 -- flg )	C	primitives.s	flg = true if n1 less than 0
0<>	( n1 -- flg )	C	primitives.s	flg = true if n1 not equal 0
0=	( n1 -- flg )	C	primitives.s	flg = true if n1 equal 0
0>	( n1 -- flg )	C	primitives.s	flg = true if n1 greater than 0
1=	( n -- flg )	C	words.s	flg = true of n=1

## MEMORY
-!	( n addr -- )	H	core.forth	decrement long at addr
!	(n adr -- )	C	primitives.s	store long b at adr
@	( adr -- n )	C	primitives.s	read long n from address adr
+!	( n addr -- )	H	core.forth	increment long at addr
c!	( b adr -- )	C	primitives.s	store byte b at adr
c@	( adr -- b )	C	primitives.s	read byte b from address adr
c+!	( n addr -- )	H	core.forth	increment byte or char at addr
cell	( -- 4 )	C	words.s	returns constant 4
cells	( n1 -- n2 )	C	ext.s	n2 = n1 x 4
cmove	( src-addr dst-addr count -- )	H	core.forth	Move count bytes from source to destination
freemem	( -- n )	H	core.forth	return free memory in bytes
heap-end	( -- )	C	words.s
heap-start	( -- )	C	words.s
heap?	( a -- flg )	H	core.forth
osfreemem	( -- n )	C	primitives.s	n = memory free for punyforth progam and data in bytes
usedmem	( -- n )	H	core.forth	return used memory in bytes

## MATHS
-	(n1 n2 -- n3 )	C	primitives.s	n3 = n1 - n2
*	(n1 n2 -- n3 )	C	primitives.s	n3 = n1 x n2
/	( n1 n2 -- quotient)	H	core.forth	n1 divided by n2, leaves quotient on stack
/mod	( n1 n2 -- rem quot )	C	primitives.s	quot = n1 / n2, remainder is rem
%	( n1 n2 -- remainder )	H	core.forth	n1 divided by n2, leaves remainder on stack
+	(n1 n2 -- n3 )	C	primitives.s	n3 = n1 + n2
1-	( n1 -- n2 )	C	ext.s	n2 = n1-1
1+	( n1 -- n2 )	C	ext.s	n2 = n1+1
abs	( n1 -- n2 )	H	core.forth	n2 = |n1|
between?	( min n2 max -- flg )	H	core.forth	flg=true if inclusively between max, min
max	( n1 n2 -- n3 )	H	core.forth	n3 = unsigned largest of n1, n2
min	( n1 n2 -- n3 )	H	core.forth	n3 = unsigned smallest of n1, n2
random	( -- n )	C	ext.s	n = random number long

## CONVERSION
>number	( str len -- number flg )	C	words.s	convert string to decimal number and flg=true if successful
hex>int	( str -- n | throws:ECONVERT )	H	core.forth	hex string str is converted to a long, else throws an ECONVERT exception
hex>int'	( str len -- n | throws:ECONVERT )	H	core.forth	part of hex>int
hexchar>int	( char -- n | throws:ECONVERT )	H	core.forth

## LOOPING
?do	( count start -- ) immediate	H	core.forth	start a counted loop, if count <> start, else don't do the loop contents
+loop	( -- )	H	core.forth
bounds	( start len -- limit start )	H	core.forth	converts start len parameters to limit start for the use by 'do'
do	( count start -- ) immediate	H	core.forth	start a counted loop structure
end?	( incr -- flg )	H	core.forth
i	( -- n )	C	primitives.s	n = do loop count
j	( -- n )	C	primitives.s	n = next outer loop count
loop	( -- ) immediate	H	core.forth	ends a counted loop structure
unloop	( -- )	H	core.forth	does the following:- r> r> r> 2drop >r

Examples:-
: test 10 0 do i . loop ; running test we display 0123456789
: test 10 0 do i . 2 +loop ; running test we display 02468
## CONDITIONAL BRANCH & LOOPING
again	immediate	H	forth.core
begin	immediate	H	forth.core
branch	( -- )	C	primitives.s
branch0	( n -- )	C	primitives.s
else	( -- ) immediate	H	forth.core
if	( flg -- ) immediate	H	forth.core
repeat	( -- ) immediate	H	forth.core
then	( -- ) immediate	H	forth.core
until	( flg -- ) immediate	H	forth.core
while	( flg -- ) immediate	H	forth.core

Examples:
if <words to execute if condition true> then	begin <more words> while <more words> repeat
if <words if condition true> else <words if condition false> then	begin <more words> until
	begin <more words> again - an endless loop

## CASE STATEMENTS
CASE statements are constructed in a manner similar to C using SWITCH, CASE, and BREAK.

case	( -- branch-counter ) immediate	H	core.forth
endcase	( #branches #branchesi*a -- ) immediate	H	core.forth
endof	( -- ) immediate	H	core.forth
of	( n -- ) immediate	H	core.forth

CASE example:-
: day ( n -- ) / case / 1 of print: "Monday" endof / 2 of print: "Tuesday" endof / 3 of print: "Wednesday" endof / 4 of print: "Thursday" endof / 5 of print: "Friday" endof / 6 of print: "Saturday" endof / 7 of print: "Sunday" endof / print: "Unknown day: " . / endcase ;

## VECTORED EXECUTION, COMBINATORS and QUOTATIONS
bi	( a xt1 xt2 -- xt1.a xt2.a )	H	core.forth	Applies quotation p to x, then applies quotation q to x.
bi@	( a b xt -- xt.a xt.b )	H	core.forth	Applies the quotation to x, then to y.
bi*	( a b xt1 xt2 -- xt1.a xt2.b )	H	core.forth	Applies the quotation to x, then to y.
dip	( a xt -- a )	H	core.forth	calls a quotation while temporarily hiding the tos
execute	( adr -- )	C	primitives.s	Execute word at adr
keep	(a xt -- xt.a a )	H	core.forth	calls a quotation with an item on the stack, restoring that item after the quotation returns.
{	immediate	H	core.forth	start a quotation - a headless Punyforth word-within-a-word
}	immediate	H	core.forth	end a quotation

## ERROR MANAGEMENT
catch	( xt -- exception | 0 )	H	core.forth
EASSERT		H	core.forth	exception type
ECONVERT		H	core.forth	exception type
EESCAPE		H	core.forth	exception type
ENOTFOUND		H	core.forth	exception type
EOVERFLOW		H	core.forth	exception type
eundef	( -- )	C	words.s	error word undefined ??
eundefc	( -- )	C	words.s
eundefi	( -- )	C	words.s
EUNDERFLOW		H	core.forth	exception type
ex-type	( exception -- )	H	core.forth
exception:	( <name> -- )	H	core.forth
throw	( i*x exception -- i*x exception | 0 )	H	core.forth
traceback	( code -- )	H	core.forth

## START-UP / SHUT DOWN / SYSTEM STATE
abort	( -- )	C	primitives.s	call forth abort
deep-sleep	( a2 -- )	C	primitives.s	place cpu in deep-sleep
os-enter-critical	( -- )	C	primitives.s
os-exit-critical	( -- )	C	primitives.s
state	( -- adr )	C	words.s	address of compiler state flag, state @ returns true if compiling
task-yield	( -- )	C	primitives.s
xpause	( -- )	C	ext.s

## I/O PORTS
adcread	( -- n )	C	ext.s	read the analogue input
gpio-mode	( direction num -- )	C	ext.s
gpio-read	( gpionum - n )	C	ext.s
gpio-set-interrupt	( inttype gpionum -- )	C	ext.s
gpio-write	( bool gpionum -- )	C	ext.s
pulse-in	( pin state timeout -- pulselen )	C	ext.s	returns pulse input length in uS
pwm-duty	( duty -- )	C	ext.s	duty is 16 bits
pwm-freq	( freq -- )	C	ext.s	freq is 16 bits
pwm-init	( pinsarray numberofpins -- )	C	ext.s
pwm-start	( -- )	C	ext.s
pwm-stop	( -- )	C	ext.s
uart-set-bps	(uartnum bps -- )	C	ext.s

## TIMING and FREQUENCY
cpufreq!	( freq -- )	C	ext.s	set cpu frequency (MHz)
cpufreq@	( -- freq )	C	ext.s	read cpu frequency (MHz)
ms	( n -- )	C	ext.s	wait n milliseconds
ms@	( -- n )	C	ext.s	get system time in milliseconds
us	( n -- )	C	ext.s	wait n uS
us@	( -- n )	C	ext.s	get system time in uS
wait-event	( delayms eventbuffer -- n )	C	ext.s

## DEFINITIONS
:	( <word> -- )	C	words.s	start forth definition
'	( -- xt | throws:ENOTFOUND )	H	core.forth	find the xt of the next word in the inputstream
[']	( -- )	C	primitives.s	compile only
['],		H	core.forth
]	( -- )	C	words.s	resume compilation mode
allot	( n -- )	C	words.s	allot n bytes of memory as part of a definition
backref,	( n -- )	H	core.forth	n is stored at here-1, here is unchanged
create:		H	core.forth
createheader	( <name> -- )	C	words.s
defer:	( <name> -- )	H	core.forth
defer!	( dst-xt src-xt -- )	H	core.forth
does>		H	core.forth
exit	( -- )	C	primitives.s	pop the forth PC from the return stack
handler		H	core.forth	defer type
interpret?	( -- flg )	H	core.forth	flg = true if currently interpreting
is:	immediate	H	core.forth
lastword	( -- adr )	C	words.s
override	( <word> -- ) immediate	H	core.forth	used to refer to the previous word of the same name. Punyforth otherwise defaults to recursion
postpone:	( -- | throws:ENOTFOUND )	H	core.forth	force compile semantics of an immediate word
prepare-forward-ref	( -- a )	H	core.forth	performs:- here 0 ,
resolve-forward-ref	( a -- )	H	core.forth	performs:- here over - swap !
unhandled		H	core.forth	defer type
var-lastword	( -- adr )	C	words.s

## RECOGNISERS
_	( addr len -- ? )	H	core.forth
chr?		H	core.forth
hex?		H	core.forth
str,	( len -- )	H	core.forth
str?		H	core.forth

## COMMENTS
(	( -- )	H	core.forth	Start a comment, must finish with ) on same line
\	( -- )	H	core.forth	The rest of the line is ignored as a comment

## COMPILE LITERALS
Bytes, words, and longs may be compiled directly into code memory usually for building fixed tables.
These cannot be used inside a definition as any preceding literal would have already been compiled as a literal.

,	( n -- )	C	words.s	compile a long as used in building tables e.g. 1 , 2 , 3 ,
c,	( b -- )	C	words.s	compile a byte or char as used in building tables e.g. 1 c, 2 c, 3 c,
c,-until	(separator -- )	H	core.forth
literal	( n -- )	C	words.s	compile tos into the word e.g. [ 4 5 + ] literal

## DEBUG
help	( -- )	H	core.forth	List all words in the dictionary
stack-hide	( -- )	H	core.forth	Set the user prompt to nothing, no stack display
stack-print	( -- )	H	core.forth	Print the data stack contents
stack-show	( -- )	H	core.forth	Set the user prompt ot show the stack contents

## CONSTANTS and VARIABLES
array:	( size <name> -- ; index -- addr )	H	core.forth	define an array of longs e.g. 10 array: myname
buffer:	( size <name> -- ; -- addr )	H	core.forth	define a block of memory as a buffer
byte-array:	( size <name> -- ; index -- addr )	H	core.forth	define an array of bytes e.g. 10 array: myname
constant:	( <name> n -- ; -- n ) )	C	words.s	define a constant value or string e.g. 3 constant: mynumber e.g. "Hello" constant: mystring
FALSE	( -- 0 )	H	core.forth
field:	( <name> count n -- count+n ; / adr1 -- adr2 )	H	core.forth	at compile: add a variable to a data structure, keeping count of total bytes storage / when run: adds the field name offset to the start address ofa record
init-variable:	( <name> n -- ; -- adr )	C	words.s	defines a variable with a preset value e.g. 23 init-variable: myinitvar
single-handler	( -- adr )	H	core.forth	single threaded global handler
struct	( -- 0 )	H	core.forth	begin definition of a data structure
TRUE	( -- -1 )	H	core.forth
var-handler	( -- adr )	H	core.forth	stores the address of the nearest exception handler
variable:	( <name> -- )	H	core.forth	Create a new long, initialised to 0

## Private Words
CALIGN	( -- )	X	PRI	long align code memory

Structure definition:- / struct / cell field: .client / cell field: .line / constant: WorkerSpace / The 'struct' word places a byte count = 0, top of stack / Each 'field:" word labels the structure member + adds to the bytes count on tos. The 'constant' word creates the constant named WorkerSpace. When WorkerSpace is called, it returns the total number of bytes in the structure. N.B. All the above has done is create a set of labels, no actual variable has been created yet .By convention, the fields are prefixed with '.' as a reminder of their role	Now we can create an actual variable with that structure:- / here WorkerSpace allot constant: Worker1 / This actually creates an 8 byte variable named Worker1 / We can store values in Worker1, using the field names to place the data properly:- / value base addr + offset store value / 12 Worker1 .client ! / 34 Worker1 .line !

## STRINGS
=str	( str1 str 2 -- flg )	H	core.forth	flg=true if str1 = str2
compare	( str1 len1 str2 len 2 -- flg )	C	words.s	flg = true id str1 = str2
str-in?	( str substr -- flg )	H	core.forth	flg=true if substr is found within str
str-starts?	( str substr -- flg )	H	core.forth	flg=true if str starts with substr
strlen	( str -- len )	H	core.forth	len is the length of string str
word	( <word> -- str len )	C	words.s	converts next word in input stream to string

Punyforth strings are null terminated and are defined without leading space e.g. "Hello world".
Thus a string constant is "This is a fine day" constant: mystring
## STREAMING I/O
From start-up Punyforth is set 115200 baud 8 bit, no parity, 1 stop bit. N.B. The line terminator is cr-lf and a local echo is necessary

_emit	( b -- )	C	primitives.s	part of emit
?	( adr -- )	H	core.forth	Display long at adr with no formatting
.	( n -- )	H	core.forth	Display n with no formatting
#tib	( -- adr )	C	words.s	returns addr of the input stream char counter. so #tib @ returns the number of chars
chr>in	( chr -- )	C	words.s	inject chr into input stream
cr	( -- )	H	core.forth	Emit a carriage return character
crlf?	( chr1 chr2 -- flg )	H	core.forth	flg=true if chr2=10 and chr1=13
emit	( chr -- )	C	words.s	display a chr e.g. $A emit or 20 emit
eschr	( char -- char )	H	core.forth	read next char from stdin
key	( -- ch | false )	C	words.s	read chr from input stream, waits if none available
link-type	( link -- )	H	core.forth	display the word name of the link on tos - used in help, tasks-print
print:	( <words within ""> -- )	H	core.forth	Print an inline string e.g. print: "hello world"
println:	( <words within ""> -- )	H	core.forth	Like print: but adds a cr
prompt	( -- adr )			return address of user prompt string
readchar		C	ext.s
readchar-nowait	( -- chr | false )	C	ext.s	read next char in input stream. If none available returns false
readchar-wait	( -- chr )	C	ext.s	wait indefinitely for next char on input stream
separator	( -- chr )	H	core.forth	Consume input stream until non-whitespace character chr
show_prompt	( -- )			enable the user prompt
space	( -- )	H	core.forth	Emit a space return character
tib	( -- adr )	C	words.s	returns addr of input stream char buffer
type	( asciiz -- )	C	words.s	display 0 terminated string
type-counted	( addr len -- )	C	words.s	display counted string
whitespace?	(chr -- flg )	H	core.forth	Is chr any of the whitespace characters?
xemit	( addr -- )	C	words.s	pointer to current 'emit' word, so that the output stream can be diverted
xtype	( addr -- )	C	words.s	pointer to current 'type' word, so that the input stream can be diverted

## DICTIONARY
compile-time		C	words.s
find	( str len -- link | false )	C	words.s	Find str in dictionary and return link else false
here	( -- adr )	C	words.s	returns address of end of dictionary space
hidden?	( link -- flg )	C	words.s
hide	( link -- )	C	words.s
immediate	( -- )	C	words.s	Mark the last word defined as executing at compile time
immediate?	( link -- flg )	C	words.s
link>body	( adr1 -- adr2 )	C	words.s
link>flags	( adr -- flags )	C	words.s
link>flb	( adr1 -- adr2 )	C	words.s
link>len	( adr -- n )	C	words.s
link>name	( adr1 -- adr2 )	C	words.s
link>xt	( adr1 -- adr2 )	C	words.s
marker:	( <name> -- )	H	core.forth	Defines a module start marker. When this word is executed, all words defined after this marker are forgotten
reveal	( link -- )	C	words.s

## I2C BUS
i2c-init	( bus sclpin sdapin freq -- result )	C	ext.s
i2c-read	( bus ack -- data )	C	ext.s
i2c-read-slave	( bus slaveaddr data buffer len -- result )	C	ext.s
i2c-start	( bus -- )	C	ext.s
i2c-stop	( bus -- flg )	C	ext.s
i2c-write	( bus byte -- flg )	C	ext.s
i2c-write-slave	( bus slaveaddr data buffer len -- result )	C	ext.s

## SPI
spi-init	( bus mode freqdiv msb endyness minimalpins -- n )	C	ext.s
spi-send	( bus outdata indata datasize wordsize -- n )	C	ext.s
spi-send8	( bus data -- n )	C	ext.s

## EEPROM
/end	( -- )	C	ext.s	Used in EEPROM resident source to signal end of file - stop reading from the file
erase-flash	( sector -- n )	C	ext.s
load	( blocknum -- )	C	ext.s
loading?	( -- flg )	C	ext.s
read-flash	( addr buffer size -- n )	C	ext.s
write-flash	( addr buffer size -- n )	C	ext.s

## WIFI
dhcpd-start	(1stclientip maxleases -- )	C	ext.s
dhcpd-stop	( -- )	C	ext.s
wifi-ip-str	( interface buffer buffsize -- )	C	ext.s	interface 0=station 1=softap
wifi-set-mode	( mode -- flg )	C	ext.s
wifi-set-softap-config	( ssid password authmode hidden channels maxconnections -- flg )	C	ext.s
wifi-set-station-config	(ssid password -- flg )	C	ext.s
wifi-softap-start	( -- flg )	C	ext.s
wifi-station-connect	( -- flg )	C	ext.s
wifi-station-disconnect	( -- flg )	C	ext.s
wifi-station-start	( -- flg )	C	ext.s
wifi-stop	( -- )	C	ext.s

## NETCON
HTTP and UDP communication:-

netbuf-data	( netbuf -- buffer size )	C	ext.s
netbuf-del	( netbuf -- )	C	ext.s
netbuf-next	( netbuf -- n )	C	ext.s
netcon-accept	( netcon -- netcon err_t )	C	ext.s
netcon-bind	( conn host port -- n )	C	ext.s
netcon-close	( conn -- )	C	ext.s
netcon-connect	( conn host port -- n )	C	ext.s
netcon-delete	( conn -- )	C	ext.s
netcon-listen	( netcon -- n )	C	ext.s
netcon-new	( contype -- n )	C	ext.s
netcon-read-timeout	( netcon timeoutsec -- )	C	ext.s
netcon-read-timeout@	( netcon - timeoutsec )	C	ext.s
netcon-recv	( netcon -- netbuf err_t )	C	ext.s
netcon-recvinto	( conn buffer size -- countread err_t )	C	ext.s
netcon-send	( conn data len -- n )	C	ext.s
netcon-set recvtimeout	( conn recvtimeoutms -- )	C	ext.s
netcon-write	( conn data size -- n )	C	ext.s

N.B port is type long, host is type string "192.168.1.8" or the name e.g. "Bob-PC"
## APPLICATIONS
ws2612set	( gpionum rgb -- )	C	ext.s
ws2812rgb	( gpionum rgb -- )	C	ext.s

## Unsorted words
_type	( string -- )	C	ext.s
[str	( -- forward-ref )	H	core.forth
>in	( -- adr )	C	words.s
>s'	( ? addr n -- addr2 ? )	H	core.forth
>str	( addr n -- )	H	core.forth
align	( -- )	C	words.s
align!	( -- )	C	words.s
dp	( -- )	C	words.s
entercol		C	words.s
enterdoes		C	words.s
eundef	( -- )	C	words.s
push-enter	( -- )	C	ext.s
str]	( forward-ref -- )	H	core.forth
var-dp	( -- )	C	words.s

# SOURCE CODE LIBRARIES on EEPROM
The following words are located in source files stored on the EEPROM. This is to economise on space in a user application, in that libraries of words that aren't used don't take up precious space in the ram. A library can be loaded into the dictionary by:-

 <library name> load e.g. WIFI load

Some libraries are dependant on others, in which case the dependancies are automatically loaded.

NAME	STACK CODE LOCATED	DESCRIPTION
        TYPE IN FILE
## DHT22
bit-at	( i -- bit )	H	dht22.forth
bits	( -- adr )	H	dht22.forth	40 byte array
bytes	( -- adr )	H	dht22.forth	5 bytes array
bytes-clear	( -- )	H	dht22.forth
checksum	( -- )	H	dht22.forth
convert	( lsbyte msbyte -- value )	H	dht22.forth
dht-measure	( -- humidity temperature )	H	dht22.forth	measures temperature and humidity using DHT22 sensor / temperature and humidity values are multiplied with 10
dht-pin	( -- gpiopin )	H	dht22.forth	read pin used by dht22
dht-pin!	( gpiopin -- )	H	dht22.forth	set pin used by dht22
ECHECKSUM		H	dht22.forth	exception
fetch	( -- )	H	dht22.forth	high pulse for 26-28 us is bit0, high pulse for 70 us is bit1
humidity	( -- humidity%-x-10 )	H	dht22.forth
init	( -- )	H	dht22.forth
measure	( -- )	H	dht22.forth
process	( -- )	H	dht22.forth
temperature	( -- celsius-x-10 )	H	dht22.forth
validate	( -- | throws:ECHECKSUM )	H	dht22.forth
var-dht-pin	( -- adr )	H	dht22.forth	1 long, initial value 2 , var-dht-pin \ default D4, wemos d1 mini dht22 shield, use dht-pin! to override

## EVENT
Event	( -- n )	H	event.forth	Record containing .type .ms .us .payload
event-timeout	( -- adr )	H	event.forth	1 long variable, initial value 70
EVT_GPIO	( -- 100 )	H	event.forth	1 long constant
next-event	( eventstruct -- event )	H	event.forth

## FLASH
b	( y -- )	H	flash.forth	block editor command - blank row
block	( block# -- addr )	H	flash.forth
buf	( -- adr )	H	flash.forth	buffer, SIZE long
c	( -- )	H	flash.forth	block editor command - clear screen
ch	( y x -- adr )	H	flash.forth
check	( code -- | flag )	H	flash.forth	flag = 0=OK,1=ERR, 2=TIMEOUT, 3=UNKNOWN
COLS	( -- 128 )	H	flash.forth	1 long constant
copy-row	( dsty srcy -- )	H	flash.forth
d	( y -- )	H	flash.forth	block editor command - delete row
dirty	( -- adr )	H	flash.forth	1 long variable, initial value FALSE
EBLOCK		H	flash.forth	exception
list	( block# -- )	H	flash.forth
offs	( -- adr )	H	flash.forth	1 long variable
p	( y -- )	H	flash.forth	block editor command - prepend empty row before row y
r	( y <line> -- )	H	flash.forth	block editor command - overwrite row
row	( y -- adr )	H	flash.forth
ROWS	( -- 32 )	H	flash.forth	1 long constant
SIZE	( -- 4096 )	H	flash.forth	1 long constant
type#	( y -- )	H	flash.forth

## FONT57
font5x7	( -- )	H	font5x7.forth	large data table containing the font patterns

## GPIO
GPIO_INTTYPE-NONE	( -- 0 )	H	gpio.forth	1 long constant - gpio interrupt type
GPIO_INTTYPE_EDGE_POS	( -- 1 )	H	gpio.forth	1 long constant - gpio interrupt type
GPIO_INTTYPE_EDGE_NEG	( -- 2 )	H	gpio.forth	1 long constant - gpio interrupt type
GPIO_INTTYPE_EDGE_ANY	( -- 3 )	H	gpio.forth	1 long constant - gpio interrupt type
GPIO_INTTYPE_LEVEL_LOW	( -- 4 )	H	gpio.forth	1 long constant - gpio interrupt type
GPIO_INTTYPE_LEVEL_HIGH	( -- 5 )	H	gpio.forth	1 long constant - gpio interrupt type
GPIO_IN	( -- 1 )	H	gpio.forth	1 long constant - gpio modes
GPIO_OUT	( -- 2 )	H	gpio.forth	1 long constant - gpio modes
GPIO_OUT_OPEN_DRAIN	( -- 3 )	H	gpio.forth	1 long constant - gpio modes
GPIO_HIGH	( -- 1)	H	gpio.forth	1 long constant - gpio values
GPIO-LOW	( -- 0 )	H	gpio.forth	1 long constant - gpio values
blink	( pin -- )	H	gpio.forth	switch pin on and off once, 0.5s period
times-blink	( pin ntimes -- )	H	gpio.forth	blink pin n times
ENOPULSE		H	gpio.forth	exception

## NETCON
UDP	( -- 1 )	H	netcon.forth	1 long constant
TCP	( -- 2 )	H	netcon.forth	1 long constant
RECV_TIMEOUT_MSEC	( -- 70 )	H	netcon.forth	1 long constant
ENETCON		H	netcon.forth	exception
ERTIMEOUT		H	netcon.forth	exception
NC_ERR_TIMEOUT	( -- -3 )	H	netcon.forth	1 long constant - netcon error
NC_ERR_CLSD	( -- -15 )	H	netcon.forth	1 long constant - netcon error
netcon-new	( type -- netcon | throws:ENETCON )	H	netcon.forth
check	( errcode -- )( errcode -- | throws:ENETCON )	H	netcon.forth
netcon-connect	( port host type -- netcon | throws:ENETCON )	H	netcon.forth	Connect to a remote port/ip. Must be used in both TCP and UDP case
netcon-bind	( port host netcon -- | throws:ENETCON )	H	netcon.forth
netcon-listen	( netcon -- | throws:ENETCON )	H	netcon.forth
netcon-tcp-server	( port host -- netcon | throws:ENETCON )	H	netcon.forth	Create a TCP server by binding a connection to the given port host. Leaves a netcon connection associated to the server socket on the stack.
netcon-udp-server	( port host -- netcon | throws:ENETCON )	H	netcon.forth	Create a UDP server by binding a connection to the given port host. Leaves a netcon connection associated to the server socket on the stack.
netcon-accept	( netcon -- new-netcon | throws:ENETCON )	H	netcon.forth	Accept an incoming connection on a listening TCP connection. Leaves a new netcon connection that is associated to the client socket on the stack.
netcon-send-buf	( netcon buffer len -- | throws:ENETCON )	H	netcon.forth	Write the content of the given buffer to a UDP socket
netcon-write-buf	( netcon buffer len -- | throws:ENETCON )	H	netcon.forth	Write the content of the given buffer to a TCP socket
netcon-write	( netcon str -- | throws:ENETCON )	H	netcon.forth	Write a null terminated string to a TCP socket
netcon-writeln	( netcon str -- | throws:ENETCON )	H	netcon.forth	Write a null terminated string then a CRLF to a TCP socket
read-ungreedy	( size buffer netcon -- count code | throws:ERTIMEOUT )	H	netcon.forth
netcon-read	( netcon size buffer -- count | -1 | throws:ENETCON/ERTIMEOUT )	H	netcon.forth	Read maximum `size` amount of bytes into the buffer. Leaves the amount of bytes read on the top of the stack, or -1 if the connection was closed.
netcon-readln	( netcon size buffer -- count | -1 | throws:ENETCON/EOVERFLOW/ERTIMEOUT )	H	netcon.forth	Read one line into the given buffer. The line terminator is CRLF. Leaves the length of the line on the top of the stack, or -1 if the connection was closed. If the given buffer is not large enough to hold EOVERFLOW is thrown.
netcon-dispose	( netcon -- )	H	netcon.forth	Close then dispose the given socket.

N.B port is type long, host is type string "192.168.1.8" or the name e.g. "Bob-PC"
## NTP - Network Time Protocol
ENTP		H	ntp.forth	exception
con	( -- adr )	H	ntp.forth	1 long variable
SIZE	( -- 48 )	H	ntp.forth	1 long constant
packet	( -- adr )	H	ntp.forth	byte array, SIZE in size
request	( -- buffer )	H	ntp.forth
connect	( port host -- )	H	ntp.forth
send	( -- )	H	ntp.forth
receive	( -- #bytes )	H	ntp.forth
dispose	( -- )	H	ntp.forth
ask	( port host -- #bytes )	H	ntp.forth
parse	( -- )	H	ntp.forth
network-time	( port host -- seconds-since-1970 | throws:ENTP )	H	ntp.forth

Example - this reads the time from your router and prints the number of seconds since start of 1970 until the ESC key is pressed
: test begin 123 "192.168.1.1" network-time . cr 1000 ms readchar-nowait 27 = until ;
## PING - ultrasound distance measurement
Measures the pulse generated by ultrasonic ranging module (tested with: HC-SR04 sensors)
Works the following way:
(1) Using IO trigger for at least 10us high level signal,
(2) The Module automatically sends eight 40 kHz and detect whether there is a pulse signal back.
(3) IF the signal comes back, time of high output IO duration is the time from sending ultrasonic to returning.
Distance = (high level time×velocity of sound (340M/S) / 2,
Usage example: PIN_ECHO 100 cm>timeout PIN_TRIGGER ping pulse>cm

emit-pulse	( trigger-pin -- )	H	ping.forth
listen-echo	( echo-pin timeout-us -- ms )	H	ping.forth
ping	( echo-pin timeout-us trigger-pin -- pulse-duration-us )	H	ping.forth
cm>timeout	( cm -- us )	H	ping.forth
inch>timeout	( inch -- us )	H	ping.forth
pulse>cm	( us -- cm )	H	ping.forth
pulse>inch	( us -- inch )	H	ping.forth

## SONOFF Smart Power Socket
RELAY	( -- 12 )	H	sonoff.forth	1 long constant
relay-state	( -- adr )	H	sonoff.forth	1 long variable, initial value FALSE
on	( -- )	H	sonoff.forth
off	( -- )	H	sonoff.forth
toggle	( -- )	H	sonoff.forth
LED	( -- 13 )	H	sonoff.forth	1 long constant
led-on	( -- )	H	sonoff.forth
led-off	( -- )	H	sonoff.forth
flash	( n -- )	H	sonoff.forth
alert	( -- )	H	sonoff.forth	flash LED 10 times

## SSD1306I2C
WIDTH	( -- 64 )	H	ssd1306-i2c.forth	1 long constant
HEIGHT	( -- 48 )	H	ssd1306-i2c.forth	1 long constant
SCL	( -- 5 )	H	ssd1306-i2c.forth	1 long constant
SDA	( -- 4 )	H	ssd1306-i2c.forth	1 long constant
RST	( -- 0 )	H	ssd1306-i2c.forth	1 long constant
SLAVE	( -- 16r3C )	H	ssd1306-i2c.forth	1 long constant
BUS	( -- 0 )	H	ssd1306-i2c.forth	1 long constant
FREQ	( -- 2 )	H	ssd1306-i2c.forth	1 long constant, 400kHz i2c speed
SIZE	( -- WIDTH HEIGHT * 8 / )	H	ssd1306-i2c.forth	1 long constant
screen1	( -- adr )	H	ssd1306-i2c.forth	buffer
screen	( -- buffer )	H	ssd1306-i2c.forth
EI2C		H	ssd1306-i2c.forth	exception
wire	( -- )	H	ssd1306-i2c.forth
check	( code -- | throws:EI2C )	H	ssd1306-i2c.forth
buf	( -- adr )	H	ssd1306-i2c.forth	two byte table
cmd	( byte -- | throws:EI2C )	H	ssd1306-i2c.forth
reset	( -- )	H	ssd1306-i2c.forth
init	( -- )	H	ssd1306-i2c.forth
width*	immediate	H	ssd1306-i2c.forth
clampx	immediate	H	ssd1306-i2c.forth
clampy	immediate	H	ssd1306-i2c.forth
clamp	( x y -- x' y' )	H	ssd1306-i2c.forth
y>bitmask	( y -- bit-index )	H	ssd1306-i2c.forth
xy>i	( x y -- bit-mask buffer-index )	H	ssd1306-i2c.forth
or!	( value addr -- )	H	ssd1306-i2c.forth
and!	( value addr -- )	H	ssd1306-i2c.forth
set-pixel	( x y -- )	H	ssd1306-i2c.forth
unset-pixel	( x y -- )	H	ssd1306-i2c.forth
pixel-set?	( x y -- flg)	H	ssd1306-i2c.forth
hline	( x y width -- )	H	ssd1306-i2c.forth
rect-fill	( x y width height -- )	H	ssd1306-i2c.forth
fill-buffer	( value -- )	H	ssd1306-i2c.forth
c1	( -- n )	H	ssd1306-i2c.forth
c2	( -- n )	H	ssd1306-i2c.forth
display	( -- )	H	ssd1306-i2c.forth
display-clear	( -- )	H	ssd1306-i2c.forth
bus-init	( -- )	H	ssd1306-i2c.forth
display-init	( -- | throws:ESSD1306 )	H	ssd1306-i2c.forth
font	( -- adr )	H	ssd1306-i2c.forth	1 long variable, initial value is 0
text-left	( -- adr )	H	ssd1306-i2c.forth	1 long variable, initial value is 0
text-top	( -- adr )	H	ssd1306-i2c.forth	1 long variable, initial value is 0
font-size	( -- adr )	H	ssd1306-i2c.forth	1 long variable, initial value is 1
font-small	( -- )	H	ssd1306-i2c.forth
font-medium	( -- )	H	ssd1306-i2c.forth
font-big	( -- )	H	ssd1306-i2c.forth
font-xbig	( -- )	H	ssd1306-i2c.forth
draw-lf	( -- )	H	ssd1306-i2c.forth
draw-cr	( -- )	H	ssd1306-i2c.forth
dot	( x y -- )	H	ssd1306-i2c.forth
stripe	( bits -- )	H	ssd1306-i2c.forth
draw-char	( char -- )	H	ssd1306-i2c.forth
draw-str	( str -- )	H	ssd1306-i2c.forth
str-width	( str -- )	H	ssd1306-i2c.forth

## SSD1306SPI
SCL	( -- 14 )	H	ssd1306-spi.forth	1 long constant
SDA	( -- 13 )	H	ssd1306-spi.forth	1 long constant
DC	( -- 2 )	H	ssd1306-spi.forth	1 long constant
RST	( -- 0 )	H	ssd1306-spi.forth	1 long constant
BUS	( -- 1 )	H	ssd1306-spi.forth	1 long constant
SPI_WORD_SIZE_8BIT	( -- 1 )	H	ssd1306-spi.forth	1 long constant
freq	( divider count -- freq )	H	ssd1306-spi.forth
DISPLAY_WIDTH	( -- 128 )	H	ssd1306-spi.forth	1 long constant
DISPLAY_HEIGHT	( -- 64 )	H	ssd1306-spi.forth	1 long constant
ESSD1306		H	ssd1306-spi.forth	exception
ESSD1306_WRITE		H	ssd1306-spi.forth	exception
BUFFER_SIZE	( -- DISPLAY_WIDTH DISPLAY_HEIGHT * 8 / )	H	ssd1306-spi.forth	1 long constant
screen1		H	ssd1306-spi.forth	buffer, size BUFFER_SIZE
actual	( -- adr )	H	ssd1306-spi.forth	1 long variable, initial value screen1
screen	( -- buffer)	H	ssd1306-spi.forth
wire	( -- )	H	ssd1306-spi.forth
check-write-result	( code -- | ESSD1306_WRITE )	H	ssd1306-spi.forth
write-command	( cmd -- | ESSD1306_WRITE )	H	ssd1306-spi.forth
display-invert	( -- )	H	ssd1306-spi.forth
display-normal	( -- )	H	ssd1306-spi.forth
RIGHT	( -- 38 )	H	ssd1306-spi.forth	1 long constant
LEFT	( -- 39 )	H	ssd1306-spi.forth	1 long constant
scroll-start	( stop-row start-row direction -- )	H	ssd1306-spi.forth
scroll-stop	( -- )	H	ssd1306-spi.forth
write-data	( data -- | ESSD1306_WRITE )	H	ssd1306-spi.forth
display-on	( -- )	H	ssd1306-spi.forth
init	( -- )	H	ssd1306-spi.forth
display-reset	( -- )	H	ssd1306-spi.forth
y>bitmask	( y -- bit-index )	H	ssd1306-spi.forth
xy-trunc	( x y -- x' y' )	H	ssd1306-spi.forth
xy>i	( x y -- bit-mask buffer-index )	H	ssd1306-spi.forth
or!	( value addr -- )	H	ssd1306-spi.forth
and!	( value addr -- )	H	ssd1306-spi.forth
set-pixel	( x y -- )	H	ssd1306-spi.forth
unset-pixel	( x y -- )	H	ssd1306-spi.forth
pixel-set?	( x y -- flg )	H	ssd1306-spi.forth
hline	( x y width -- )	H	ssd1306-spi.forth
rect-fill	( x y width height -- )	H	ssd1306-spi.forth
fill-buffer	( value -- )	H	ssd1306-spi.forth
display	( -- )	H	ssd1306-spi.forth
display-clear	( -- )	H	ssd1306-spi.forth
display-init	( -- | ESSD1306 )	H	ssd1306-spi.forth
font	( -- adr )	H	ssd1306-spi.forth	1 long variable, initial value is 0
text-left	( -- adr )	H	ssd1306-spi.forth	1 long variable, initial value is 0
text-top	( -- adr )	H	ssd1306-spi.forth	1 long variable, initial value is 0
font-size	( -- adr )	H	ssd1306-spi.forth	1 long variable, initial value is 1
font-small	( -- )	H	ssd1306-spi.forth
font-medium	( -- )	H	ssd1306-spi.forth
font-big	( -- )	H	ssd1306-spi.forth
font-xbig	( -- )	H	ssd1306-spi.forth
draw-lf	( -- )	H	ssd1306-spi.forth
draw-cr	( -- )	H	ssd1306-spi.forth
dot	( x y -- )	H	ssd1306-spi.forth
stripe	( bits -- )	H	ssd1306-spi.forth
draw-char	( char -- )	H	ssd1306-spi.forth
draw-str	( str -- )	H	ssd1306-spi.forth
str-width	( str -- )	H	ssd1306-spi.forth

## TASKS
Punyforth supports cooperative multitasking which enables users to run more than one task simultaneously.

.handler		H	tasks.forth	field within structure
.ip		H	tasks.forth	field within structure
.next		H	tasks.forth	field within structure
.r0		H	tasks.forth	field within structure
.rp		H	tasks.forth	field within structure
.s0		H	tasks.forth	field within structure
.sp		H	tasks.forth	field within structure
.status		H	tasks.forth	field within structure
activate	( task -- )	H	tasks.forth	used within a task to enter the task in the round robin tasks list
alloc-rstack	( -- a )	H	tasks.forth
alloc-stack	( -- a )	H	tasks.forth
choose	( -- )	H	tasks.forth
current	( -- adr )	H	tasks.forth	1 long variable, initial value REPL
deactivate	( -- )	H	tasks.forth	used within a task to remove itself from the tasks list
last	( -- adr )	H	tasks.forth	1 long variable, initial value REPL
multi	( -- )	H	tasks.forth	switch to multi-task mode
multi-handler	( -- a )	H	tasks.forth
mutex	( -- )	H	tasks.forth
pause		H	tasks.forth	deferred word, initially set to 'nop'
pause-multi	( -- )	H	tasks.forth	pause is set to execute this word, when multi is run
PAUSED	( -- 0 )	H	tasks.forth	1 long constant
r0-multi	( -- top-rstack-adr )	H	tasks.forth
REPL	( -- adr )	H	tasks.forth	1 long constant, returning the address of the 1st 'Task' entry in the linked list of tasks
restore	( -- )	H	tasks.forth
s0-multi	( -- top-stack-adr )	H	tasks.forth
save	( sp ip rp -- )	H	tasks.forth
semaphore	( -- )	H	tasks.forth
signal	( semaphore -- )	H	tasks.forth
single	( -- )	H	tasks.forth	switch to single-task mode
SKIPPED	( -- 1 )	H	tasks.forth	1 long constant
stop	( task -- )	H	tasks.forth
switch	( task -- )	H	tasks.forth
Task		H	tasks.forth	structure
task-find	( task -- link )	H	tasks.forth
task-rstack-size	( -- adr )	H	tasks.forth	1 long variable, initial value 112
task-stack-size	( -- adr )	H	tasks.forth	1 long variable, initial value 112
task:	( user-space-size <name> -- ; -- task )	H	tasks.forth
tasks-print	( -- )	H	tasks.forth
user-space	( -- a )	H	tasks.forth
wait	( semaphore -- )	H	tasks.forth

Example - to have a task running in the background:- / 0 task: mytask \ create a task, no local variables needed / : some-infinite-loop ( task -- ) / activate / begin / println: "Still running..." / 1000 ms / pause / again / ; / multi \ switch to multitask mode / mytask some-infinite-loop \ this will run the task in the background / \ while the prompt is still active	Example - to have a task run every n milliseconds in the background:- / : elapsed? ( clock delay -- clock' flg ) \ need a timer that doesn't block / over + ms@ <= \ read cpu clock again / dup if \ more than delay elapsed? / nip ms@ swap \ yes, replace clock value / then \ flg=true if delay has elapsed / ; / : print1000ms \ will run every 1s / activate / ms@ \ read the clock in miliseconds / begin / 1000 elapsed? \ has 1s elapsed since we last read / \ the clock? / if / println: "print1000ms running" / then / pause / again / deactivate \ never executes, actually / ;

Example - Task runs every n milliseconds, n times only:- / : print10timesonly / activate / s0 sp! r0 rp! \ found necessary else both stacks creep / 10 ms@ / begin / 2000 elapsed? / if / println: "print10timesonly running" / swap 1- swap / then / pause / over 0= / until / drop drop deactivate / ;	Running print10timesonly and print100ms together :- / 0 task: task1 / 0 task: task2 / multi / task1 print100ms / task2 print10timesonly / After 20s print10timesonly stops running, but can be restarted with:- / task2 print10timesonly / Use single to stop all

## MAILBOX
Often tasks need to communicate with each other. A mailbox is a fixed size blocking queue where messages can be left for a task. Receiving from an empty mailbox or sending to a full mailbox blocks the current task.

mailbox:	( size -- )	H	mailbox.forth
mailbox-send	( message mailbox -- )	H	mailbox.forth
mailbox-receive	( mailbox -- message )	H	mailbox.forth

## TCP-REPL
To set Punyforth to work with a telnet terminal:-
1. Set up the wifi connection with	wifi-connect "yourpassword" "yourrouterssid" this will report an IP address and port given
2. Load the REPL over TCP module with	TCPREL load
3. Start the remote terminal session	repl-start
4. On the remote PC, open a telnet session to the ip address the router gave Punyforth e.g 192.168.1.8 on port 1983
5. Remember that local echo and CR / LF are needed to terminate a line

HOST	( -- wifi-ip )	H	tcp-repl.forth	1 long constant
PORT	( -- 1983 )	H	tcp-repl.forth	1 long constant
client	( -- adr )	H	tcp-repl.forth	1 long variable, initial value 0
line	( -- adr )	H	tcp-repl.forth	buffer, size 128
connections		H	tcp-repl.forth	mailbox
repl-server-task		H	tcp-repl.forth	task
repl-worker-task		H	tcp-repl.forth	task
type-composite	( str -- )	H	tcp-repl.forth
emit-composite	( chr -- )	H	tcp-repl.forth
eval	( str -- i*x )	H	tcp-repl.forth
server	( task -- )	H	tcp-repl.forth
command-loop	( -- )	H	tcp-repl.forth
worker	( task -- )	H	tcp-repl.forth
repl-start	( -- )	H	tcp-repl.forth

## TURNKEY
SIZE	( -- 4096 )	H	turnkey.forth	1 long constant
BOOT_ADDR	( -- 16r5100 )	H	turnkey.forth	1 long constant
ETURNKEY		H	turnkey.forth	exception
boot		H	turnkey.forth	deferred word
dst	( -- n )	H	turnkey.forth
heap-size	( -- n )	H	turnkey.forth
check	( code ( code -- | ETURNKEY )	H	turnkey.forth
n,	( addr n -- addr+strlen )	H	turnkey.forth
s,	( str-dst str-src -- str-dst+strlen )	H	turnkey.forth
save-loader	( -- )	H	turnkey.forth
turnkey	( -- )	H	turnkey.forth

## WIFI

NULL_MODE	( -- 0 )	H	wifi.forth	1 constant long
STATION_MODE	( -- 1 )	H	wifi.forth	1 constant long
SOFTAP_MODE	( -- 2 )	H	wifi.forth	1 constant long
STATIONAP_MODE	( -- 3 )	H	wifi.forth	1 constant long
MAX_MODE	( -- 4 )	H	wifi.forth	1 constant long
AUTH_OPEN	( -- 0 )	H	wifi.forth
AUTH_WEP	( -- 1 )	H	wifi.forth
AUTH_WPA_PSK	( -- 2 )	H	wifi.forth
AUTH_WPA2_PSK	( -- 3 )	H	wifi.forth
AUTH_WPA_WPA2_PSK	( -- 4 )	H	wifi.forth
AUTH_WPA_WPA2_PSK	( -- 5 )	H	wifi.forth	??
EWIFI		H	wifi.forth	exception
>ipv4	( octet1 octet2 octet3 octet4 -- n )	H	wifi.forth
check-status	( status -- | throws:EWIFI )	H	wifi.forth
wifi-connect	( password ssid -- | throws:EWIFI )	H	wifi.forth	Connect to an existing Wi-Fi access point with the given ssid and password. / For example: "ap-pass" "ap-ssid" wifi-connect
wifi-softap	( max-connections channels hidden authmode password ssid -- | throws:EWIFI )	H	wifi.forth	Creates an access point with the given properties. For example: / 172 16 0 1 >ipv4 wifi-set-ip / 4 3 0 AUTH_WPA2_PSK / "1234567890" "my-ssid" wifi-softap / 8 172 16 0 2 >ipv4 dhcpd-start / max-connections should be <= max-leases
ip	( interface -- str )	H	wifi.forth
wifi-ip	( -- str )	H	wifi.forth	station ip
softap-ip	( -- str )	H	wifi.forth	station ip

# Document version
Version 1.2	Some MULTI words descriptions added
Version 1.1	Examples highlighted red + some extra examples added - October 2020
Version 1.0	Initial version based on Punyforth v0.5, compiled by Bob Edwards, SW U.K. Ham radio callsign G4BBY - October 2020